## Slide 1: Mini oscilloscope
PWM Signal Drawer using :
ATMega32A Microcontroller
GLCD ( ks0108 )
AMIT Graduation Project Presented by: Eng. Ali Muhammad
Emb.61
alimuhammadabuamer@gmail.com

## Slide 2: Layered Architecture
APPLICATION Layer
Hardware Abstraction Layer
Microcontroller Abstraction Layer
App.h
glcd.h
icu.h
pwm.h
dio.h

## Slide 3: FlowChart
Initialization
Measure Signal
Draw Signal
PWM
ICU
GLCD
ICU
GLCD

## Slide 4: Measure Signal
ICU_GetSignal();
Clear Input Capture Flag Set Trigger Edge: RISING_EDGE
Wait for Input Capture →
Set value to A
Clear Input Capture Flag Set Trigger Edge: Falling_EDGE
Wait for Input Capture →
Set value to c
Wait for Input Capture →
Set value to B
Clear Input Capture Flag Set Trigger Edge: RISING_EDGE
Period time = B-A high Time = C-B
Duty = Ton / T ;

## Slide 5: Draw Signal
Draw_Signal();
GLCD_DisplayString();
Get duty cycle from ICU
GLCD Line 0: Display Frequency Value in kHz
GLCD Line 6: Display Arrow on First Cycle Period Time
GLCD Line 7: Display the PWM signal shape
GLCD Line 4: Display Period Time Value in milliseconds.
GLCD Line 0: Display Duty Cycle Value in %.
repeat

## Slide 6
Start
Initialization
Get signal
Draw time arrow
loop sync
I continue
stop
end

## Slide 7: Special Patterns on Graphical LCD

## Slide 8: Thank you !